Generators

- Smaller generators – such as the one pictured below will be allowed on campus in the designated areas that have been predetermined by the Office of Fire Safety - no closer than 10 feet to any university building.  Metal barriers or caution tape (below) must be placed around the generator(s) to prevent pedestrians from accidentally entering hazardous areas.

- Generators MUST be shut down before refueling - no "hot pumping" on campus.

- No movie production vehicles will be allowed to park in the following: Red Fire Lanes, Green Zones, White Zones. Yellow Zones may be used for loading / unloading.

LOS ANGELES FIRE DEPARTMENT & USC FIRE SAFETY

GENERATOR REFUELING

SEFETY CHECKLIST & SPECIAL INSTRUCTIONS

SEC. 57.05.20. PERMITS – REQUIRED.

No person, firm, or corporation shall engage in any specific action or project for which a Permit is required by this section without first having obtained a valid Division 5 Permit from the Department. Generator refueling requires an LAFD permit.

SPECIAL INSTRUCTIONS:

- Vehicles and equipment should be protected from vehicle traffic.

- No person shall smoke or produce any open flame within 50 feet of any point where fuel is being transferred.

- Approved hoses and valves for pressurized gases.

- Flammable liquids and gases kept 25 feet away from heat sources.

- No refueling of generators or other equipment while in operation. No hotfueling.

- Generators grounded or insulated

- Refueling done in approved area.

- Refueling vehicle must possess a valid/current LAFD Division 5 permit.

- Proper ventilation to prevent flammable vapors from accumulating.

- The parking brake shall be set and chock blocks shall be placed in such a manner as to prevent the forward or backward motion of the vehicle whenever it is parked, left unattended by the driver, or during loading and unloading operations.

- Each tank vehicle shall be equipped with at least one approved portable fire extinguisher having a 2A, 20B:C classification in accordance with Division 140 of this article. Portable fire extinguishers shall be kept in good operating condition at all times, and shall be located in an accessible place on each tank vehicle.

When refueling at USC please provide the following information to USC Fire Safety:

Primary contact:

Title:

Phone number(s):

Name of person who will be refueling:

Phone Number:

LAFD Division 5 permit obtained and accessible? Yes 		  No

For help obtaining LAFD permits please call USC Fire Safety

Jeff Pendley (213) 740-6838 or Rob Forsberg (213) 440-0381.

Please e-mail a completed copy of this form to USC Fire Safety at pendley@usc.edu