|  | USC Fire Safety and Emergency Planning |
| --- | --- |
|  | May not obstruct or conceal (in whole, or even in part) any emergency routes, signage, or devices — such as exits, exit lights, fire alarm pull boxes, fire hose cabinets, fire extinguishers, sprinkler heads, smoke detectors, etc. Must be made from non-flammable material, or treated with a flame-retardant solution or process approved by the State Fire Marshal. |
|  | All holiday trees must be kept out of corridors, and away from doorways and heat sources. Flame-retardant – Cut natural trees shall be flame-retardant treated in accordance with Title 19, C.C.R., and a State Fire Marshal Certificate of Flame Resistance Tag shall be attached near the base. Cut natural trees must be kept in water at all times to slow the natural drying process. |
|  | Lights must bear the Underwriters Laboratory (UL) seal of approval. Be certain that there are no loose sockets, and that wires are not frayed or damaged. Do not run wiring through doorways, under carpeting, or through holes in walls. Do not use zip cord extension cords — we recommend using a multiple outlet power strip, with an internal circuit breaker. Never plug one extension cord into another. Always turn the holiday lights off when you leave the building. |
|  | Candles and open flame devices are not permitted. Do not decorate the corridor with wrapping paper. Dispose of all decorations, trees, and wrappings immediately after the holidays by taking them to campus dumpster areas. |
|  | For additional copies please go to the USC Fire Safety web site: |
|  | http://capsnet.usc.edu/FireSafety |

LOS ANGELES FIRE DEPARTMENT

DIVISION 22

COMBUSTIBLE DECORATIONS

SEC. 57.22.04. CHRISTMAS TREES AND DECORATIONS.

(Amended by Ord. No. 170,060, Eff. 11/14/94.)

A. In buildings, tents, premises, or portions thereof, to which the public is admitted or invited, Christmas trees and decorations shall comply with the provisions of this subsection.

1. Christmas Trees - The base of cut natural trees shall be kept in water or wet sand.

2. Flame-retardant – Cut natural trees shall be flame-retardant treated in accordance with Title 19, C.C.R., and a State Fire Marshal Certificate of Flame Resistance Tag shall be attached near the base.

3. Decorations – All decorations used on Christmas trees shall be non-combustible or flame-retardant and shall meet the requirements of Title 19, C.C.R. No open flame device shall be used. All electrical equipment shall be of an approved type.

4. Field Test for Fire Resistance – The Chief may, at any time, take samples from

any Christmas tree or decoration and field test the specimen in accordance with L.A.F.D. Standard No. 66. The field test shall be performed in a safe location, using a common flame applied for 12 seconds of exposure to the sample. During the exposure, flaming shall not spread over the complete length of the sample, or in excess of four inches from the bottom of the sample for larger sample sizes. Afterflame shall not be more than two seconds. Materials which break and drip flaming particles shall be considered hazardous. Christmas trees or any decorations determined by the Chief to be a fire hazard shall be

immediately removed from the building.

5. Location - Christmas trees shall be located clear of exits and aisles and in an area separated from ordinary combustibles by a distance not less than the height of the tree.

6. Stability – Christmas trees shall be secure and stable in their position.

7. Fire Protection – An approved fire extinguisher in accordance with Division 140 of this article shall be available.

8. Permit – A Special Permit shall be required for any storage, display, sale, or other use of Christmas trees within buildings where more than 10 trees are located.

9. Artificial Trees - Manufactured trees which are constructed of metallic, noncombustible or fire-resistive materials may be used. Artificial and live Christmas trees are subject to field test procedures.

10. Lighting - Lighting of metallic or otherwise electrically conductive trees shall

be done a minimum of six feet away from the tree and plainly visible from the area used to light the tree. All lighting used for illumination of trees shall be Underwriters Laboratories listed or other approved type.

B. Every person conducting, managing or operating a Christmas tree sales business, whether exclusively or in conjunction with the sale of other goods, wares or merchandise, shall attach, or cause to be attached, a Fire Safety Tag to each tree greater than two feet tall and having a base greater than one inch in diameter prior to the sale of such tree.

The tag shall be securely affixed to the tree and shall have the following statements, as a minimum, printed on it:

1. Make a fresh cut on the bottom of the tree; place in a reservoir tree stand filled

with water.

2. Water Christmas tree daily.

3. Test your smoke detectors.

4. Never use lights with frayed cords or empty sockets.

5. Mini-lights are safest; they produce less heat.

6. Do not use candles on or near tree.

7. Turn off all Christmas lights prior to leaving your home or going to bed.

8. Safely dispose of your tree before it becomes dangerously dry.

9. Never burn your tree or any part of it in a fireplace.

10. Pick-up/drop-off disposal services offered by the Bureau of Sanitation, Phone

No. ___________________.

The above-referenced telephone number shall be obtained from the Fire Department.

All statements shall be on one side of the tag. In the event a language other than English is the primary language of the majority of persons residing within one-half mile of the location of the business, the same statements shall be printed on the reverse side of the tag in that language. Tags shall have a minimum width of 3 inches and a minimum length of 7 inches. The text of the tag shall be at least 12 points in size in conventional font. Tags must be made of 30 lb. weight stock paper or equivalent. Each tag shall have a hole at the top to receive a wire-tie, plastic tie or other material that can be used to attach the tag securely to the tree.