## Slide 1: Light Search and Rescue Operations
USC CERT Basic Training

## Slide 2: Unit 7 Objectives
Identify and apply CERT size-up requirements for potential search and rescue situations
Demonstrate common techniques for light search and rescue
Demonstrate safe techniques for debris removal and survivor extraction during search and rescue operations

## Slide 3: Unit 7 Topics
Search and Rescue Size-up
Conducting Interior and Exterior Search Operations
Conducting Rescue Operations

## Slide 4: Search and Rescue
Search and rescue consists of three separate operations
  Size-up: Using 9-step, continual model
  Search: Locating survivors and documenting
  Rescue: Extricating survivors

## Slide 5: Deciding to Attempt Rescue
Rescue attempt decisions are based on three factors
  Risks involved for the rescuer and survivor
  Greatest good for the greatest number
  Resources and manpower available

## Slide 6: Goals of Search and Rescue
Rescue greatest number in shortest amount of time
Get walking wounded out first
Rescue lightly trapped survivors next
Keep the rescuers and survivors safe

## Slide 7: Effective Search and Rescue
Depends on:
  Effective size-up
  Rescuer safety
  Survivor safety

## Slide 8: CERT Size-up
Gather Facts
Assess Damage
Consider Probabilities
Assess Your Situation
Establish Priorities
Make Decisions
Develop Plan of Action
Take Action
Evaluate Progress

## Slide 9: Size-up Step 1
Gather Facts:
  Time of event and day of the week
  Construction type/terrain
  Occupancy
  Weather
  Hazards
  Search subject profile

## Slide 10: Size-up Step 2
Assess and Communicate Damage
  The CERT mission changes if damage is light, moderate, or heavy

## Slide 11: Light Damage
Superficial
Broken windows
Superficial cracks or breaks in wall surface
Minor damage to the interior contents
Safe to enter and remain

## Slide 12: Moderate Damage
Visible signs of damage
Decorative work damaged or fallen
Many visible cracks or breaks in wall
Major damage to interior contents
Building still on foundation
Enter only to save lives

## Slide 13: Heavy Damage
Partial or total collapse
Tilting
Obvious structural instability
Building off foundation
Smoke, fire, gas leaks, or hazardous material
Rising water
DO NOT enter a building with heavy damage under ANY CIRCUMSTANCES!

## Slide 14: Size-up Step 3
Consider Probabilities:
  How stable is the situation?
  What secondary factors should be considered?
  What else could go wrong?
  What does it mean for the search and rescue?

## Slide 15: Size-up Step 4
Assess Your Situation:
  Is the situation safe enough to continue?
  What risks will rescuers face?
  What resources are needed?
  What resources are available?

## Slide 16: Rescue Resources
Personnel:
  CERT Team
  Bystanders you can use for first aid
Tools:
  Crowbars
Equipment:
  Cribbing equipment

## Slide 17: Size-up Step 5
Establish Priorities:
  What should be done?
  In what order?
  How do you rescue the greatest number in the shortest amount of time?

## Slide 18: Size-up Step 6
Make Decisions:
  Keep in mind:
    Safety of CERT members
    Life safety for survivors and others
    Protection of the environment
    Protection of property

## Slide 19: Size-up Step 7
Develop Plan of Action:
  Focus operation on established priorities and decisions
  Provide documentation to give to responding agencies
  Provide documentation to become part of CERT records

## Slide 20: Size-up Step 8
Take Action:
  Base action on plan developed during Step 7

## Slide 21: Size-up Step 9
Evaluate Progress:
  Most critical step
  Monitor plan’s effectiveness and safety

## Slide 22: Structural Voids
If you see collapsed floors or walls, GET OUT!

## Slide 23: Structural Voids
Pancake Void

## Slide 24: Structural Voids
V Void

## Slide 25: Structural Voids
Lean-To Void

## Slide 26: Individual Voids
Survivors may seek protection in various places
  Inside bathtubs
  Underneath desks
  Inside cabinets
  Under/next to beds
  Inside closets

## Slide 27: Search Markings (1 of 3)
Upon entering search area:
  Make a slash
  Enter info
Upon leaving search area:
  Complete ‘X’
  Enter info

## Slide 28: Search Markings (2 of 3)
What information do you mark?

## Slide 29: Search Markings (3 of 3)
Sample

## Slide 30: Building Markings (3 of 3)
Sample
GAS OFF
Gold Team
MISC
TIME IN: 1430 hrs
TIME OUT: 1520 hrs

## Slide 31: Search Methodology (1 of 5)
Remain within arm’s reach of one other CERT member
Call out to survivors, “If anyone can hear my voice, come here”
Ask any survivors who do respond for more information about the building or others who may be trapped
Survivors might be in shock or confused

## Slide 32: Search Methodology (2 of 5)
Bottom-up/top-down for a multi-story building
Right wall/left wall for a single floor
Stop frequently to listen

## Slide 33: Search Methodology (3 of 5)
Stop frequently to listen for:
  Tapping
  Movement
  Voices

## Slide 34: Search Methodology (4 of 5)
Triangulation allows rescuers to view a location from several perspectives

## Slide 35: Search Methodology (5 of 5)
Keep records of rescued survivors and of those who remain trapped or who are dead
Report information to DPS

## Slide 36: Exterior Search
Set up a grid search:
  Set distance between searchers according to visibility and debris
  Overlap patterns for full coverage
  Search in as straight a line as possible
  Mark areas that have been searched

## Slide 37: Rescue Operations
Remove objects and debris to free survivors and create safe rescue environment
Assess survivors
Remove survivors

## Slide 38: Creating a Safe Environment
Maintain rescuer safety
Assess survivors in lightly and moderately damaged buildings
Evacuate survivors as quickly as possible

## Slide 39: Precautions to Minimize Risk
Know your limitations
Follow safety procedures
Remove debris by leveraging and cribbing

## Slide 40: Proper Lifting Procedures
Back straight
Bend knees
Keep load close to body
Push up with legs

## Slide 41: Leveraging and Cribbing
For heavy lifting
Performed in tandem
Helps extricate survivors
Various materials and objects may be used

## Slide 42: Leveraging and Cribbing

## Slide 43: Leveraging and Cribbing

## Slide 44: Leveraging and Cribbing

## Slide 45: Two Types of Removal
Self removal or assist; and
Lifts and drags

## Slide 46: Which Extrication Method?
Extraction method depends on a number of criteria
  General stability of the immediate environment
  Number of rescuers available
  Strength and ability of the rescuers
  Condition of survivor

## Slide 47: Stair Chair
Survivor sits in the chair strapped in
CERT members carefully glide survivor down the stairs

## Slide 48: One-Person Arm Carry
Lift around survivor’s back and under his or her knees
Lift survivor by keeping your own back straight and lifting with your legs

## Slide 49: Pack-Strap Carry

## Slide 50: Two-Person Carry

## Slide 51: Chair Carry

## Slide 52: Flexible Stretcher Carry

## Slide 53: Blanket Drag

## Slide 54: Hands On….
Remember:
Safety First!!!
Search & Rescue Training
Cribbing Training
Stair Chair Training